## Slide 1
Summary
Standard 6 & Historic Preservation
Rehabilitation Standards, Local Government Impact & Materials Conservation

## Slide 2
Rehabilitation Standards at a Glance
Standard 2
Retain Character
Preserve character-defining features; avoid removing distinctive materials or altering spatial relationships
Standard 3
No False History
Do not introduce conjectural features or elements from other properties that create a false sense of development
Standard 6
Repair Before Replace
Repair deteriorated features rather than replace; match original design, color, texture, and materials when replacement is needed
Standard 7
Gentlest Methods
Use the least damaging treatments possible; avoid methods that cause harm to historic materials

## Slide 3
Why Standard 6 Matters for Local Government
Legal & Regulatory Alignment
Aligns with CEQA, NEPA (National Environmental Policy Act), Section 106 (Section 106 of the National Historic Preservation Act of 1966 (NHPA) and CLG programs
Simplifies environmental review process
Provides consistent, defensible decision framework
Funding & Tax Credits
Qualifies projects for federal and state rehabilitation tax credits
Supports CLG certification and grant eligibility
Non-compliance risks losing credibility with SHPO and NPS
Sustainability Goals
Less waste, less embodied carbon, longer building lifespans
Complements green building and climate resilience strategies
Repair-first approach reduces environmental impact
Community Character
Preserves authentic look and feel of historic neighborhoods
Supports community identity, tourism, and property values
Maintains integrity of historic districts and landmarks

## Slide 4
Materials & Deterioration
Deterioration Factors
Understanding the rate and mechanism of deterioration guides repair decisions.
External Factors
Storms and earthquakes
Graffiti and vandalism
General human interaction
Internal Factors
Corrosion of embedded metals (e.g., rebar rust causing spalling)
Chemical reactions within materials over time
Material fatigue and natural aging
Masonry & Plaster
Includes stone, brick, terrazzo, plaster, terracotta, and concrete.
Common Patterns
Cracking and surface fractures
Detachment and delamination
Spalling from corroded internal anchors
Key Distinction
Sacrificial elements (mortar joints) are designed to be replaced periodically
Character-defining features (cast elements, ornamental work) require preservation or careful restoration

## Slide 5
GUIDING PRINCIPLES
Key Principles & Next Steps
Core Principles
Repair before replacement is the default under Standard 6
Documentary evidence is required before replacing any historic feature
Use the gentlest treatment methods to preserve original fabric
Never introduce conjectural features that create a false sense of history
Assess the rate and mechanism of deterioration, not just its presence
Next Steps for Commissioners
1
Review your local ordinance
Confirm it references the Secretary of the Interior Standards and aligns with Standard 6 requirements
2
Audit recent decisions
Check whether past approvals consistently applied repair-before-replace criteria under Standards 2, 3, 6, and 7
3
Strengthen documentation requirements
Require applicants to provide evidence of deterioration severity and explain why repair was ruled out
4
Coordinate with SHPO
Ensure your CLG program stays aligned with state and federal expectations to protect certification and funding